## Slide 1: Making Presentations That Stick
A guide by Chip Heath & Dan Heath

## Slide 2: Introduction to DMA
Direct Memory Access (DMA) allows hardware to access system memory without needing the CPU.
Increases system efficiency and speed.
Reduces CPU workload by handling data transfers directly.

## Slide 3: How DMA Works
DMA controller manages data transfer directly between devices and memory.
Steps:
CPU initiates the DMA transfer.
DMA controller takes control of the system bus.
Data transfers between the device and memory.
CPU is notified when the transfer is complete.

## Slide 4: Types of DMA
Modes:
  Burst Mode: Transfers entire blocks of data at once.
  Cycle Stealing: Transfers byte-by-byte, alternating with CPU cycles.
  Transparent Mode: Transfers occur only when the CPU is idle.
  Demand Mode: Waits for a ready signal from the device before transferring data.

## Slide 5: Advantages of DMA:
Efficiency: Reduces CPU load, allowing the CPU to perform other tasks while the DMA handles data transfer.
Speed: Faster than programmed I/O since DMA transfers data directly between memory and peripheral devices.
Resource Management: Allows simultaneous data processing, enabling the system to handle more tasks at once.
Disadvantages of DMA:
Complexity: More intricate design is required for implementing DMA.
Cost: Additional circuitry is needed for DMA, which adds to the system cost.
Conflicts: Increased risk of bus contention due to potential multiple devices attempting access simultaneously.

## Slide 7: Key Features of Advanced DMA
Scatter-Gather DMA: Efficiently handles non-contiguous memory for fragmented scenarios.
Chain Transfers: Automates sequential transfers, reducing CPU involvement.
Coherent Memory DMA: Maintains memory consistency between CPU and memory.
Prioritization and Arbitration: Assigns priorities to ensure critical task servicing.

## Slide 9
.
●

## Slide 10
// DMA Control Block
struct dma_cb
{
uint32_t ti; // Transfer information
uint32_t src_addr; // Source address
uint32_t dest_addr; // Destination address
uint32_t length; // Transfer length
uint32_t stride; // Stride (set to 0)
uint32_t next_cb; // Next control block (set to 0 for no chaining) uint32_t padding[2]; // Padding to make it 32 bytes
};

## Slide 11: Overview of Registers in UART-DMA Driver
UART Registers
UART_DR_OFFSET (Data Register)
  Purpose: Stores data for UART transmission/reception.
  Function: Data is transferred to/from this register during UART operations.
UART_DMACR_OFFSET (DMA Control Register)
  Purpose: Controls DMA operations for UART.
  Function: Enables/disables DMA and configures transfer settings.
DMA Registers
DMA_CONBLK_AD_OFFSET (Control Block Address Register)
  Purpose: Holds the address of the DMA Control Block.
  Function: Points to DMA settings (source/destination addresses, length).
DMA_CS_OFFSET (Control & Status Register)
  Purpose: Provides DMA transfer status.
  Function: Indicates transfer completion or errors.

## Slide 12: API,s for UART-DMA
Memory Mapping and I/O Functions
ioremap()
Purpose: Maps physical memory addresses to virtual memory for kernel access.
ioread32()
Purpose: Reads 32-bit data from a mapped I/O register.
iowrite32()
Purpose: Writes 32-bit data to a mapped I/O register.
Memory Allocation and Management
dma_alloc_coherent()
Purpose: Allocates physically contiguous memory for DMA operations.
dma_free_coherent()
Purpose: Frees memory allocated by dma_alloc_coherent().

## Slide 13: It’s no surprise Marcos uses Google Translate in his shop regularly.
There are 23 officially recognized languages in the EU.
theguardian.com
Tip
Don’t let data stand alone. Always relate it back to a story you’ve already told, in this case, Marco’s shop.